NAME
    E100PKT 0.2, packet driver for DOS

SYNOPSIS
    E100PKT <option>

DESCRIPTION
    E100PKT is a basic packet driver for Intel's 8255x family of
    Ethernet adapters. It should work with any PCI device that
    Linux's e100 kernel module (in e100.c) does.

    Options are case-insensitive and must begin with either a / or -.
    All the program's input and output is in hex without a leading
    "0x" (e.g. "60" is 96 decimal).

SYSTEM REQUIREMENTS
    * An IBM PC or compatible
    * An Intel 80386 or compatible processor
    * DOS 2 or higher
    * 2560 bytes of free conventional memory
    * An Intel E100 Ethernet adapter. That is, a PCI device whose
      vendor id is 8086 and device id is one of the following:

        1029    103c    1057    1091    27dc
        1030    103d    1059    1092
        1031    103e    1064    1093
        1032    1050    1065    1094
        1033    1051    1066    1095
        1034    1052    1067    1209
        1038    1053    1068    1229
        1039    1054    1069    2449
        103a    1055    106a    2459
        103b    1056    106b    245d

OPTIONS
    /h
    /?
        Show usage.
    /v
        Show version.
    /u
        Unload the packet driver from memory.
    /i <int_no>
        Load the packet driver into memory at the specified software
        interrupt. Valid interrupt numbers are: 60-66, 68-6f, or
        7b-7e (inclusive).
    /d
        Dump PCI configuration space to E100.PCI
        Dump EEPROM to E100.EEP
        Dump CSR to E100.CSR

BUGS
    * E100PKT cannot be loaded high.
    * E100PKT uses too much memory.
    * E100PKT cannot be unloaded if its hardware interrupt vector
      has been hooked since loading it.
    * Please send any feedback and bug reports to <sethsimon@sdf.org>.

HOME PAGE
    gopher://sdf.org/1/users/sethsimon/e100pkt/ has the latest
    version and links to technical documentation.

COPYRIGHT
    Copyright (C) 2018, Seth Simon <sethsimon@sdf.org>.

    E100PKT comes with ABSOLUTELY NO WARRANTY. This is free software
    covered by GNU GENERAL PUBLIC LICENSE 3, and you are welcome to
    redistribute it under certain conditions. See http://www.gnu.org
    or COPYING file for details.